## Slide 1
ADVATEK LABS
Up to eight dry-contact buttons for bench testing
DIRECT CONTACT · EDITABLE DIAGRAM
Bench or same-enclosure wiring only · Never apply 5 V, 12 V, 24 V or PoE to a GPIO
PoE module
Waveshare
ESP32-S3-ETH
W5500 Ethernet
16 MB flash · 8 MB PSRAM
GPIO1
Button 1
GPIO2
Button 2
GPIO15
Button 3
GPIO16
Button 4
GPIO18
Button 5
GPIO38
Button 6
GPIO39
Button 7
GPIO40
Button 8
GND
One button = one 2-core cable (twisted pair): GPIO signal + GND return
Normally open: closing the button connects its GPIO to GND
Notes: [Sources]
- https://www.waveshare.com/wiki/ESP32-S3-ETH
- https://files.waveshare.com/wiki/ESP32-S3-ETH/ESP32-S3-ETH-Schematic.pdf
- Local project source: docs/HARDWARE.md

## Slide 2
ADVATEK LABS
Add protection for a fixed indoor button cable
ONE CHANNEL · REPEAT AS NEEDED
PoE module
Waveshare
ESP32-S3-ETH
W5500 Ethernet
16 MB flash · 8 MB PSRAM
3V3
GPIO16
GND
10 kΩ pull-up
1 kΩ series
FIELD TERMINAL
+ SA5.0CA TVS
100 nF
to GND
1N5817 clamps
3V3 + GND
Dry-contact button
ONE TWISTED PAIR
The 10 kΩ resistor defines the open state. The 1 kΩ resistor limits fault current. The capacitor filters brief spikes; firmware still handles mechanical debounce.
Suitable for a fixed indoor prop · This circuit still shares ESP32 ground
Notes: [Sources]
- https://documentation.espressif.com/projects/esp-hardware-design-guidelines/en/latest/esp32s3/schematic-checklist.html
- https://www.waveshare.com/wiki/ESP32-S3-ETH
- Local project source: docs/PROTECTED-CONTACT-INPUTS.md

## Slide 3
ADVATEK LABS
Group isolation is the recommended event setup
POE-POWERED · UP TO EIGHT BUTTONS
WAVESHARE / POE SIDE
ISOLATED FIELD-BUTTON SIDE
PoE network
PoE module
Waveshare
ESP32-S3-ETH
W5500 Ethernet
16 MB flash · 8 MB PSRAM
5V / GND
3V3
GPIOs
B0505S
isolated 5V → 5V
8-channel PC817 board
3.3 V
outputs
isolated
inputs
Button 1
Button 2
Button 3
+ repeat to Button 8
One twisted pair per button
ISO COM return
ISO COM must never join Waveshare GND
Power and meter-test every channel over USB before connecting PoE
Notes: [Sources]
- https://www.mornsun-power.com/html/pdf/B0505S-1WR3.html
- https://www.waveshare.com/wiki/ESP32-S3-ETH
- Local project source: docs/PROTECTED-CONTACT-INPUTS.md